## Slide 1: ENGG7807 Thesis Progress Seminar
Optimisation Super project
Tim Mahoney

## Slide 2: Brain Computer Interfacing

## Slide 3: What are the challenges?
Difficult to get clean signal (heaps of noise, non-invasive…)
Hardware requirements – many channels, gell, preporation time
Difficult to classify
We don’t fully understand the brain

## Slide 4: Electroencephalography (EEG)

## Slide 5: Previous Studies

## Slide 6: Feature Selection for Brain Computer Interface using Particle Swarm Optimisation and Genetic Algorithm
Scope:
design for online use
aims to reduce complexity and possibly hardware requirements by only taking information needed to classify signal.
Matlab

## Slide 7: Project Timeline
Currently on track:
  Preprocessing – complete
  Feature Extraction – complete
  Feature Selection – research into algorithms and performance indicators complete
Next Step: Implement GA and PSO
Preprocessing
Feature Extraction
Feature Selection
Classification

## Slide 8: Physionet – EEG Motor Imagery/Movement Dataset
Subjects undertake a number of movement / imagery tasks during EEG recordings
Task 2 – Subject imagines opening/closing left/right fists
109 Subjects, 3x2 minute recordings each with annotations
64 Channel EEG sampled at 160 Hz
The goal is to classify left and right imagery in the EEG data

## Slide 9: Artefact Removal
Examples of EEG artefacts:
  Blinks
  Electromyography (EMG)
  Mains coupling
  Electrode shift
Removal techniques:
  Epoch removal
  Filtering
  Independent Component Analysis (ICA)
Automated Artefact Removal (AAR)
Preprocessing
Feature Extraction
Feature Selection
Classification

## Slide 10: Independent Component Analysis
Voice in a crowd
Labelled 3000 samples PHD candidates helped
Implemented FastICA algorithm on MATLAB

## Slide 11: Results
Preprocessing
Feature Extraction
Feature Selection
Classification

## Slide 12: Features
Feature Extraction:
  Surface Laplacian Transform
  Filter into frequency bands
  Downsample about event to attain ERD/ERS
Results in 2009 feature long vector
Preprocessing
Feature Extraction
Feature Selection
Classification
Ch1
alpha
t-2
t-1
beta
Channels
x41
Frequency Bands
x7
Time Samples
x7

## Slide 13: Particle Swarm Optimisation
Particles move around the search space toward a heuristic optimum solution to an objective function using communication and memory.
Binary PSO
Preprocessing
Feature Extraction
Feature Selection
Classification
Wang L, et al. A Novel Probability Binary Particle Swarm Optimisation Algorithm and Its Application, 2008

## Slide 14: Genetric Algorithm
Candidate solutions span the search space by passing on strong binary traits and undergoing mutation with the hope of finding an approximately optimal solution.
Well suited to feature selection applications due to binary nature.
Preprocessing
Feature Extraction
Feature Selection
Classification

## Slide 15: Optimisation Performance
Filter method
Performance metrics:
  Correlation
  Maximum Relevance Minimum Redundancy (MRmR)
Advantages:
  Faster
  Use with any classifier
  Helps in identifying (non)important features
Preprocessing
Feature Extraction
Feature Selection
Classification

## Slide 16: Classifiers
Using three classifiers:
  Support Vector Machine,
  Artificial Neural Network and
  Random Forrest
Can be used to compare with previous studies:
  Alomari M et al. achieved 97.1% and 86.5% classification accuracy using SVM and ANN on the same dataset!
Preprocessing
Feature Extraction
Feature Selection
Classification

## Slide 17: Further research
Other datasets
Live EEG-BCI data collection
Thankyou for listening!
Questions?